## Slide 1
Silicon frontline

## Slide 4: NCV91621 : Power module
HSS ( PMOS)
Expected: WTotalPmos = Ng x Wdevice x Nb_Pmos = 10000 x 30 x 2 = 600000
599760 / 30 = 19992 in fact, 8 gates are missing ( 4 per devices)

## Slide 5: NCV91621 : Power module
LSS ( NMOS)
Expected: WTotalNmos = Ng x Wdevice x Nb_Pmos = 10000 x 27 x 2 = 540000
540108 / 27 = 20004 we have 4 extra gates ( 2 per devices)

## Slide 6
To run R3D , enter the following command in console :
> r3d xxxx.cfg
Output file (xxxx.log) is created and saves the results of the run.

## Slide 7
To run simulation, R3D requires differents kind of files :
  GDS file containing layout
  Configuration file which contains a series of R3D commands specifying simulations condition and options ( *.cfg)
  Rule file : describe layer connectivity and device recognition statements (1)
  Stack layer file : resistivity of metal, via resistance (2)
  Process file description : stack of layers : dielectric or metal, layers thickness (3)

## Slide 8
Config file
# specify GDSII file name input layout.gds # specify rule file rulefile techno.rule # specifiy mapping and techno file techfile stack_layer process # Specify lowest and uppermost metal layers r3d_start_layer metal1 r3d_end_layer metal6 # specify device specific channel resistance [Ohm*um] ( total Wgate) r3d_device_resistance 5000.0 # number of nodes for discretization of transistor along gate width r3d_mesh_for_device size=1.0 # discretizations of metals and vias r3d_mesh_for_via dx=1 dy=1 # mesh for top contact discretization r3d_mesh_for_top_contacts 40 # r3d_mesh_for_cont size=5.0 # Define contacts (wirebond or bump ) r3d_top_contact v=0.0 xc=0 yc=73 dx=20 dy=20 r=0 source name=s circular node=src r3d_top_contact v=0.1 xc=0 yc=-70 dx=20 dy=20 r=0 drain name=d circular node=drn # Set the total current through the device r3d_total_current 4.0 # create output file used by r3ddraw r3d_dat_file 2 # enables calculation of individual contributions from all resistive layers to the total resistance of the device (Rdson + interconnect) r3d_rdson_table # direct solver r3d_solver 2 # via grouping ( reduce the geometrical complexity of the layout) viagr 1

## Slide 9
Stack layers
process r3d_onc18gen2 deposition *----------------------------------------------- * No Type p/n Name Thickn. Epsilon *----------------------------------------------- step 1 substrate field 0.57 3.9 step 2 metal diff 0.12 *step 3 dielectric p fox 0.0 3.9 *step 4 dielectric p gox 0.005 3.9 step 5 metal poly 0.25 *step 6 dielectric n oxspr *step 7 dielectric n nitspr *step 8 dielectric n liner step 9 dielectric p ox1 0.71 3.9 step 10 metal metal1 0.56 step 11 dielectric p ox2 0.88 3.9 step 12 metal metal2 0.56 step 13 dielectric p ox3 0.88 3.9 step 14 metal metal3 0.56 step 15 dielectric p ox4 0.88 3.9 step 16 metal metal4 0.56 step 17 dielectric p ox5 0.88 3.9 step 18 metal metal5 0.56 step 19 dielectric p ox6 0.88 3.9 step 20 metal metal6 3.07 step 21 dielectric p ox6 ??? ??? *----------------------------------------------- enddeposition endprocess

## Slide 10
Process file
pro_layer=diff ext_layer=sd sheet_res=15;
pro_layer=poly ext_layer=poly sheet_res=6.5 TC1=0.0037;
pro_layer=metal1 ext_layer=met1 sheet_res=0.078 TC1=0.0036;
pro_layer=metal2 ext_layer=met2 sheet_res=0.078 TC1=0.0036;
pro_layer=metal3 ext_layer=met3 sheet_res=0.078 TC1=0.0036;
pro_layer=metal4 ext_layer=met4 sheet_res=0.078 TC1=0.0036;
pro_layer=metal5 ext_layer=met5 sheet_res=0.078 TC1=0.0036;
pro_layer=metal6 ext_layer=met6 sheet_res=0.010 TC1=0.0036;
ext_cont=diff_cont res=15 unit_area=0.0484;
ext_cont=poly_cont res=9 unit_area=0.0484;
ext_cont=via1 res=5 unit_area=0.0676;
ext_cont=via2 res=5.4 unit_area=0.0676;
ext_cont=via3 res=5.4 unit_area=0.0676;
ext_cont=via4 res=5.4 unit_area=0.0676;
ext_cont=via5 res=2.6 unit_area=0.1296;

## Slide 11
Layer mapping
LAYER aa 102 LAYER cont 5 LAYER met1 6 LAYER met2 18 LAYER met3 39 LAYER met4 48 LAYER met5 56 LAYER met6 79 LAYER poly 4 LAYER via1 17 LAYER via2 19 LAYER via3 47 LAYER via4 55 LAYER via5 60
bulk = extent gate_poly = poly and aa sd = aa not poly poly_cont = poly and cont diff_cont = aa and cont
connect met6 met5 by via5 connect met5 met4 by via4 connect met4 met3 by via3 connect met3 met2 by via2 connect met2 met1 by via1 connect met1 sd by diff_cont connect met1 poly by poly_cont connect bulk bulk
DEVICE MN(nmos) gate_poly poly(g) sd(s) sd(d) bulk(b) []

## Slide 12
r3d_mesh_for_device: specifies the discretization ( fracturing) of transistor along the channel width
r3d_mesh_for_device 50 : Each individual device channel is divided into 50 elements.
r3d_mesh_for_device count=50 : Each individual device channel is divided into 50 elements.
r3d_mesh_for_device size=10.0 Each individual device channel is divided into channel widths of 10.0 μm.
r3d_mesh_for_top_contacts : Discretization of the area on and around top contact
Using this command will ensure that large metal plates are meshed sufficiently where top contacts are placed on them.
r3d_mesh_for_top_contacts 20 -> A mesh of 20 equidistant spacings in both x and y directions are placed across each top contact.
r3d_start_layer & r3d_stop_layer : defines the name of the lowest and uppermost metal layer included in the simulation
r3d_start_layer metal1
r3d_end_layer metal6
Poly layer does not typically carry current, so mesh of the POLY layer is not useful. This saves RAM and simulation time.

## Slide 13
r3d_solver : specifies which matrix solver is used
Syntax : r3d_solver 0 / 1 / 2
0: if the memory size is limited, iterative mode still be preferable
2: Direct solver is faster than an iterative
r3d_channel : specifies a model for the device instanceswhich matrix solver is used
r3d_channel r=5000 rd = 0.03 rs = 0.05
r : resisivity of the channel [ohm x Wtotal in µm ]
rd or rs : serie drain / serie source resistance (Ohm per one micron of gate width)
r3d_mesh_for_via : Discretization of via
r3d_mesh_for_via 100 200 Each via layer is additionally discretized by a uniform mesh of 100 intervals along X axis and 200
intervals along Y axis.
r3d_mesh_for_via dx=5.0 dy=5.0 Each via layer is additionally discretized by a uniform mesh with a step size of 5.0 μm
along X axis and along Y axis.

## Slide 14
r3d_top_contact : specifies the top contact (wirebond, bump …)
r3d_top_contact v=0.1 xc=1040 yc=1180 dx=50 dy=50 r=0 drain name=d circular node=drn
r3d_top_contact v=0.0 xc=1040 yc=352 dx=50 dy=50 r=0 source name=s circular node=src
xc & yc : center of contact and dx & dy are width and height of the area
r3d_top_contact v=0.1 x1=265 y1=1114 x2=1882 y2=1257 r=0 drain name=d polygon node=drn layer=metal6
r3d_top_contact v=0.0 x1=265 y1=605 x2=1882 y2=748 r=0 source name=s polygon node=src layer=metal6
x1, y1,y2 ,y2 : lower left and upper right corners of the area
viagr : enables grouping if vias to reduce the geometrical complexity of the layout
0 : via grouping is disabled
1: via grouping is enabled
Via grouping is performed in order to reduce the number of vertical resistive elements corresponding to vias and contacts, ideally without loss of accuracy in the simulations. Vias and contacts forming large arrays are grouped into polygons that are discretized using a mesh. Simulating a large layout with large number of via arrays with parameter 0 (zero) may fail due to a large matrix size.

## Slide 15
r3d_total_current : specifies the total current througt the device
r3d_total_current 4.0
Analysis of current density (electromigration) by viewing results of processing current density pltos in R3DDRAW
Em rules files may be defined to set current densisty limits of backend layers ( EM rules)
include emrules

## Slide 16
Viewer
R3DDRAW

## Slide 17
https://bbs.eetop.cn/thread-625278-1-1.html
https://pdfs.semanticscholar.org/d9c4/18fcc3443e7332bea8da067bbf394abe7551.pdf