## Slide 1: Back end Digital Flow
Basics
Patrice Delpy 2018

## Slide 2: TEST introduction
TEST of a circuit, what does that mean?
A task to know
If a manufactured circuit works well or not (functional or faulty) If a circuit has faults or not
Why test a circuit? To improve and guarantee its reliability (its quality): an indispensable condition for material for medicine, automotive, aviation, etc. To ensure better production

## Slide 3
We do not try to detect any design errors We are not trying to identify the cause of the malfunction We are talking about GO / NOGO test The two main objectives are: minimize the number of failed parts not detected minimize the duration of the test (a few seconds at the most).

## Slide 4: Time in money
Reduce the number of test vectors Order the test vectors Apply the tests first: Which detect the most defects Which detect the most likely faults Having the smallest application time

## Slide 5: Test patterns generation
The generation of test vectors consists in determining the stimuli to apply at the input of a circuit to highlight a potential fault. The generation of test vectors can be performed at different levels of modeling: - At the circuit description level - Taking into account faults

## Slide 6: Test vector generation methods
Exhaustive
Random
Structural

## Slide 7: Faults simulation

## Slide 8: Testability ? Design for Test techniques
Objective : facilitate controllability and observability of internet nodes,
Add circuitery (extra hardware) allowing circuit testable

## Slide 13: Liberty files
Foreach cell of a library, these files describe:
  The ports (input and output, power)
  The type of cells : buffer, inverter, and gate, io pads , …
  The operating condition
  The power consumption (optional)
  The timing modelling
These Liberty files are given by the foundry

## Slide 14: Timing constaints (Sdc)
The sdc files (Synopsis Design Constraints) describe all the timing information between your design and the outside:
  what are the clocks signals? What are the relation between clocks ?
  what is the delay between the signals and the clock?
  What is the input or output capacitance load ?
  What are the timing exceptions ?
  …..
By default, the time unit is the ns

## Slide 15: Multi-Mode Multi-Corner view
Multi Mode :
  The chip have different functional modes (different clock speed, enable bit configuration, …)
  => One or more constraint modes associated with sdc files for each mode
Multi Corner
  There is different library set (process corner typical, slow, fast, …) and RC corners for timing analysis (propagation delay, SI analysis)
  => Each delay corners combine liberty (.lib) for the std cells and QRC techfiles for the nets
=> MMMC view file combines constraint modes and delay corners to define different scenarios (“Analysis View”)
These analysis views are used for setup analysis and the hold during STA

## Slide 16
SDC files
Setup / Hold
Clock
Inputs
Outputs
Timing exceptions

## Slide 17: Setup and hold timing (1)
The setup and hold timing checks are needed for proper propagation of data through the sequential cells. These checks verify that the data input is stable at the active clock edge.
Setup time = minimum time with data stable before clock edge
Hold time = minimum time with data stable after clock edge

## Slide 18: Setup and hold timing (2)

## Slide 19: Summary of Innovus flow

## Slide 20: More informations:
About sdc :
  “Static Timing Analysis for Nanometer Designs : a Practical Approach”
  from J . Bhasker and Rakesh Chadha

## Slide 21: Place and route ?
Process of taking a structural file
(Verilog in our case) and making a physical view
from that description. It involves placing the cells on the chip, and routing the wiring connections
between those cells.

## Slide 22
Digital Implementation System:
A Cadence tool for creation of digital
integrated circuits. This includes floor planning, power planning, test and place and route.

## Slide 23: Innovus design flow

## Slide 24
CTS: clock buffers will be added
Garantees that clock tree will be routed in the most effcient way and thereby clock skew will be reduced (best case 0)

## Slide 25: Technology and design files
LEF: library exchange format

## Slide 26: Warning !
The sdc files guide the digital tools during synthesis,
placement and routing to avoid setup or hold failure.
So be careful when you write them !
All path should be constrained to enable their analysis.
=> Unconstrained path can lead to “hidden” timing violations or “over design”

## Slide 28: LEF: Libray exchange format
An ASCII data format, used to describe a standard cell library includes the design rules for routing and the Abstract of the cells, no information about theinternal netlist of the cells
Technology: layer, design rules, via definitions, metal capacitance
  type: Layer type can be routing, cut (contact), masterslice (poly, active), overlap.
  width/pitch/spacing rules
  direction
  resistance and capacitance per unit square
  antenna Factor
2. Site: Site extension
３．Macros: cell descriptions, cell dimensions, layout of pins and blockages, capacitances.

## Slide 29: TLF : timing lib format
Ascii representation of the timing and power parameters accociated with any cell in technology
Timiing models to calculate
I/O delay path
Timing check value
Interconnect delays

## Slide 30: Engenering change order (ECO) cells
ECOs usually are done after place and route.
It’s not necessary to regenerate all-masks. Only front end layers, is known as a “Metal Fix”
Spare cells without functionakity are added during design

## Slide 31: Filler and tap cells
Must be inserted in empty areas in rows
Ensure well and diff mask continuity
Provide dummy poly for scaled technologies
Include moscap beetween VDD and GND
Called Decaps cells

## Slide 32
Wells taps needed to ensure local body voltage
Eliminate latchup
Every 30um

## Slide 33: Signal integrity (SI)
NanoRoute engine provides concurrent timing driven and SI driven routing.
Signal Integrity during routing is synonymous with Crosstalk
A switching signal may affect a neighboring net.
The switching net is called the Aggressor
The affected net is called the Victim

## Slide 34
Two major effects:
Signal slow down
  When the aggressor and victim switch in opposite directions.
Signal speed up
  When the aggressor and victim switch in the same direction.

## Slide 35: solutions
Limit length of parallel nets
Wire spreading
Shield special nets
Upsize driver or buffer

## Slide 37: Antenna fixeing

## Slide 38: Timing driving placement
Timing-driven placement tries to place critical path cells close together to reduce net RCs and to meet setup timing

## Slide 39
ftp://ftp.dii.unisi.it/pub/users/vignoli/old/elettronicaiii/seminario_ing_affortunati_2000/des_flow.pdf a voir

## Slide 40
http://www.eng.biu.ac.il/temanad/files/2017/03/02-Terminology-2012-13-A.pdf
http://www.eng.biu.ac.il/temanad/files/2017/02/Lecture-4-Standard-Cell-Libraries.pdf
http://www.ee.virginia.edu/~mrs8n/soc/SynthesisTutorials/sprflow.pdf
http://www.ee.ncu.edu.tw/~jfli/vlsidi/lecture/soc