## Slide 1: Current Mirror

## Slide 2: A MOS Transistor Biased by a Resistive Divider
Sensitivity to VDD, resistor variations, and temperature.

## Slide 3: Basic Current Mirror
A ratio of device dimensions.
No dependence on process
and temperature.
Same length MUST
be used for M1 and M2

## Slide 4: Current Mirror Used to Bias a Differential Amplifier
Reduce gm by reducing current rather than the aspect ratio.
Reduce I(M3) and I(M4).

## Slide 5: Example
W/L=10.95um/2um
W/L=21.9um/2um

## Slide 6: Trade-Offs
Output resistance (1/gds)
CDS
W/L
Current

## Slide 7: IOUT=100 uA
L(um) | W(um) | GDS (uS) | CDS (fF)
2 | 109.63 | 51.82 | 100.39
800n | 47.4 | 56.5 | 17.13
180n | 17.02 | 92.9 | 1.079
120n | 13.33 | 147 | 0.411
For Same IOUT,
L↓→W↓→GDS↑(Ro↓) →CDS ↓
Drop in Ro is not desired.

## Slide 8: Use Cascode to Increase output Resistance
Rout is approximately gm3ro3ro2
L1=L2, but L3 need not equal to L2.
Design Criteria: Choose Vb so that VY and VX.

## Slide 9: Cascode Current Source
Requirement: Choose Vb so that VX=VY
VN=VGS0+VX=VGS3+VY
Therefore, VGS3=VGS0
Since ID1=ID2, (W/L)3=(W/L)0

## Slide 10: Cascode Current Mirror
VDS1=249.6 mV
VDS6=263.7 mV
VDS5=0.675 V
VDS0=0.286 V
IDS5=20.41uA
IDS0=10 uA
gmovergds_5=47
gds6=10.35uS
Rout=4.5 MOhms
(Mismatch)
(Close)

## Slide 11: Sensitivity of IOUT due to VOUT
As VX decreases from VDD,
M3 enters the triode region first.
M2 enters the triode region

## Slide 12: Sweep Output Voltage
VTH5=177.6 mV
VG5=535.7 mV
VG6=249.6 mV
VTH6=136.9 mV

## Slide 13: VB Versus VX
VTH5=177.6 mV
VG5=535.7 mV
VG5-VTH5=535.7 mV-177.6 mV=358.1 mV
T5=SAT
T6=SAT
T5=Triode
T6=SAT
VG6=249.6 mV
VTH6=136.9 mV
VG6-VTH6=
249.6 mV-136.9 mV=112.7 mV
VB=112.7 mV →T6=Triode

## Slide 14
T5=SAT
T6=SAT
T5=Triode
T6=SAT
T5=Triode
T6=Triode

## Slide 15: Accuracy and Voltage Headroom Trade-Off
Vb is chosen to allow minimum VP.
Problem: VX is not equal to VY
Iout is not equal to Iref.
Vb is chosen to allow VX=VY
VP is not minimum.
But Iout is equal to Iref.

## Slide 16: Design Criteria
Desirables:
  IOUT should be IREF. (i.e. VX=VY)
  Vout should be minimized. (i.e. VOD2+VOD3)
VOUT=VOD3+VOD4
VA=VB→IOUT=mIREF

## Slide 17: Low Voltage Cascode
To keep M2 in saturation: Vx>Vb-Vth→Vx+Vth2>Vb
To keep M1 in saturation: VA>Vx-Vth1
Since VA=Vb-VGS2, Vb>Vx-Vth1+VGS2
Design criteria for M2

## Slide 18: Vb Requirement
Vb=VOD3+VGS4 to produce a minimum output
Voltage of VOD3 and VOD4.
By design, VGS4=VGS2, VA=VB
Vb=VOD2+VTH2+VOD1.

## Slide 19: Minimum Vout

## Slide 20: Minimum Vout
VOD3=0.163 V
VOD4=0.056 V
VOUT(min)=VOD3+VOD4=0.219 V

## Slide 21: Vb Generation (Option 1)
Requirement:
Vb=VOD2+VTH2+VOD1
VGS5=VGS2
VOD1=VGS6-I1Rb
Problem: M5 suffers from no body effect
M2 suffers from body effect
Rb is not well controlled,
unless Rb is off-chip.

## Slide 22: Vb Generation (Option 2)
Requirement:
Vb=VOD2+VTH2+VOD1
VGS5=VGS2
VOD1=VGS6-VTH7
Problem: M5 suffers from no body effect
M2 suffers from body effect
Design M7 (Large W7/L7) so
that VGS7 is approx. VTH7

## Slide 23: Vb Generation Circuit

## Slide 24: Iout versus Vout

## Slide 25: Active Current Mirror

## Slide 26: Differential Pair with Current-Source Load
Calculate the Av via Norten Equivalent Circuit
(The half-circuit concept is not applicable due to lack of symmetry)

## Slide 27: Transconductance
Gm=gm1/2

## Slide 28: Output Resistance of a Source Degenerated Amplifier
(Output Resistance)

## Slide 29: Output Resistance

## Slide 30: Differential Pair with Current-Source Load

## Slide 31: Combine Drain Currents to Increase Gain

## Slide 32: Output DC Voltage
With perfect symmetry VX,DC=VY,DC.
VX=VDD-|VGS3|
If VY < VX, then IM2<IM1.
Since IM3=IM1 and IM4=IM2,
IM3>IM4. This is not possible because
VSD4>VSD3, so IM4> IM3.

## Slide 33: Small Signal Gain
The swing at X is low since the impedance at X is 1/gm3.
So the X can be approximated as an AC ground for the
purpose calculating Gm.

## Slide 34: Rout
When a voltage is applied to the output to measured Rout,
the gate voltage of M4 does not remain constant.

## Slide 35: Active Current Mirror

## Slide 36: Voltage Gain of Active Current Mirror
Vin,pp=2 mV
Vout,pp=46.69 (Simulation)
Vout,pp=47.21 mV (Analytical calculation)

## Slide 38: Common Mode Operation

## Slide 39: Gain By Inspection (Review)
Interpretation: The resistance at the drain
Divided by the resistance in the source path

## Slide 40: Equivalent Circuit
(neglected)

## Slide 41
Vout,pp=0.003414m V
Vin,pp=2 mV
Av=0.001707

## Slide 42: Common Mode Rejection Ratio

## Slide 43: Active Current Mirror
CMRR=23.6/0.0017=13.88 x103=82.84 dB