## Slide 1: Lab4 Scan Reorder in SOC Encounter
Pro: Chia-Tso Chao
TA: Szu-Pang Mu
Hao-Wen Hsu
2011/6/9

## Slide 2: Outline
Introduction
SOC Encounter
  Scan reorder after Nanoroute
  Scan reorder during placement

## Slide 3: Introduction
In this lab, we use SOC Encounter’s build-in features to perform scan reorder either during placement or after placement.
Cadence Soc Encounter is the most common Auto Placement & Route (APR) tool, which supports both interactive command input and GUI interface.

## Slide 4
SoC Encounter Scan Design Flow
Import Design
Netlist (verilog)
Timing constraint (sdc)
Scan chain Info in DEF Format
1
Standard Cell Placement
Nano Route
6
Output File
7
IO Assignment (io)
Capacitance Table (captbl)
Cell Library
Netlist for LVS and Simulation
(verilog)
Floorplan
2
Powerplan
3
4
Power Line Connection
5

## Slide 5
DFT compiler to SOC Encounter
DC
write –f verilog –hierarchy \ –output “design_dft.v”
write_sdc \
design.sdc
design_dft.v
design.def
Soc Encounter
defIn design.def
Simulation
Library
loadConfig design.conf
design.sdc
write_scan_def \
-output design.def

## Slide 6: Outline
Introduction
SOC Encounter
  Scan reorder after Nanoroute
  Scan reorder after placement

## Slide 7: Invoke SOC Encounter
$ source /CAD/scripts/default.csh
  Just type above command for setting up all the tools.
$ source /CAD/cadence/CIC/soc.cshrc
  Just type above command for the first time invoke SOC encounter.
$ cd lab4
$ tar -zxvf lab4.tar.gz
$ encounter

## Slide 8: Import Design (1/2)
View s38584_seq.conf to check the full included file list.
Below is a snapshot:
  set rda_Input(ui_netlist) "s38584_scan.v"
  set rda_Input(ui_netlisttype) {Verilog}
  set rda_Input(ui_topcell) {s38584_seq}
  set rda_Input(ui_timelib,max) "lib/l90sprvt_bc.lib lib/uk90giosp25gpir_bc.lib“
  set rda_Input(ui_timelib,min) "lib/l90sprvt_wc.lib lib/uk90giosp25gpir_wc.lib"

## Slide 9: Import Design (2/2)
Import the design configuration
  encounter> loadConfig s38584_seq.conf
Read Scan chain information
  encounter > defIn s38584_scan.def
Check Design
  checks for missing or inconsistent library and design data at any stage of the design
  encounter > checkDesign -all
Check Unique
  checks the uniqueness of the netlist; if the netlist is unique, the result is 1
  encounter > checkUnique -verbose

## Slide 10: Floor Plan
Specify core width, height and core margin
  encounter > floorPlan -site core -s 315.0 315.0 100 100 100 100
    -s coreW coreH coreToLeft coreToBottom coreToRight coreToTop
Connect Global Nets
  encounter > globalNetConnect VDD -type tiehi -pin VDD
  encounter > globalNetConnect GND -type tielo -pin GND

## Slide 11: Power Plan (1/2)
Create core power ring
  encounter > addRing -center 1 -around core -nets {GND VDD } -width_left 9 -width_right 9 -width_bottom 9 -width_top 9 -spacing_bottom 0.34 -spacing_top 0.34 -spacing_right 0.34 -spacing_left 0.34 -layer_bottom metal3 -layer_top metal3 -layer_right metal2 -layer_left metal2

## Slide 12: Power Plan (2/2)
Create power stripes
  encounter > addStripe -block_ring_top_layer_limit metal3 -padcore_ring_bottom_layer_limit metal1 -set_to_set_distance 100 -xleft_offset 40 -xright_offset 40 -padcore_ring_top_layer_limit metal3 -spacing 0.34 -merge_stripes_value 0.28 -direction vertical -layer metal2 -block_ring_bottom_layer_limit metal1 -width 9 -nets {GND VDD}
  encounter > addStripe -block_ring_top_layer_limit metal4 -padcore_ring_bottom_layer_limit metal2 -set_to_set_distance 100 -ybottom_offset 40 -padcore_ring_top_layer_limit metal4 -spacing 0.34 -merge_stripes_value 0.28 -direction horizontal -layer metal3 -block_ring_bottom_layer_limit metal2 -ytop_offset 40 -width 9 -nets {GND VDD}

## Slide 13: Standard Cell Placement(1/4)
Connect core power pin
  “sroute” : Connects the pad pin to rings
  encounter > sroute -connect {padPin}
Specify Placement Blockage
  Choose M2, M3. Then there will be no cell placed under strip
  encounter > setPrerouteAsObs {2 3}

## Slide 14: Standard Cell Placement(2/4)
Use command “placeDesign” to do standard cell placement
  By default, “placeDesign” performs timing-driven placement with scan reordering.
  Turning scan reorder off by
    setPlaceMode -reorderScan false
  Ignore scan connection by
    setPlaceMode -ignoreScan true
  Turning Pre-placement optimization off with -noPrePlaceOpt
  encounter > placeDesign -noPrePlaceOpt

## Slide 15: Standard Cell Placement(3/4)
Connect standard cell power line from power rings or power stripes
  encounter > sroute -connect { corePin }
View scan chain
  This command display each scan chain in GUI interface
  encounter > displayScanChain

## Slide 16: Nano Route(1/3)
Runs routing via or wire optimization using the NanoRoute router.
  Use command “getNanoRouteMode” to get the current setting
  “-global | -detail | -globalDetail”
    Specify routing types by parameter
    Default: -globalDetail
  Turing on Timing and SI driven feature by
    encounter > setNanoRouteMode -routeWithTimingDriven true
    encounter > setNanoRouteMode -routeWithSIDriven true

## Slide 17: Nano Route(2/3)
  Default it runs placement check before route, turn it off by parameter “-noPlacementCheck”
  Taking care Process Antenna Issue
    encounter > setNanoRouteMode -routeInsertAntennaDiode true
    encounter > setNanoRouteMode -routeAntennaCellName ANTENNA
  encounter > routeDesign -globalDetail

## Slide 18: Nano Route(3/3)
NanoRoute Summary
#Total wire length = 369903 um.
#Total half perimeter of net bounding box = 297569 um.
#Total wire length on LAYER metal1 = 9908 um.
#Total wire length on LAYER metal2 = 75459 um.
#Total wire length on LAYER metal3 = 100147 um.
#Total wire length on LAYER metal4 = 66449 um.
#Total wire length on LAYER metal5 = 61405 um.
#Total wire length on LAYER metal6 = 31693 um.
#Total wire length on LAYER metal7 = 15988 um.
#Total wire length on LAYER metal8 = 6045 um.
#Total wire length on LAYER metal9 = 2810 um.
#Total number of vias = 99388

## Slide 19: Scan Reorder(1/3)
Use command “scanReorder” to reorders the scan cells after running placement
  “-allowSwapping”
    Allows the software to swap scan elements between scan chains within the same partition.
    Default: No
  “-lowEffort | -mediumEffort | -highEffort”
    Specifies the effort level for reordering scan chains.
    Default: mediumEffort

## Slide 20: Scan Reorder(2/3)
  “-preferH | -preferV”
    Specifies the preferred direction for scan reordering connections.
    Default: No prefer.
  “-skipNone | -skipBuffer | -skipTwoPinCell”
    Specifies how scan reordering handles buffers and inverters in the scan chain.
    Default: -skipNone
  encounter > scanReorder

## Slide 21: Scan Reorder(3/3)
*** Summary: Scan Reorder
INFO: Finished reorder 20 scan groups.
Initial total scan wire length: 39023.200
Final total scan wire length: 23139.640
Improvement: 15883.560 percent 40.70

## Slide 22: Re-do Nano Route(1/2)
For connecting the Reordered scan cell.
  encounter > routeDesign -globalDetail

## Slide 23: Re-do Nano Route(2/2)
#Total wire length = 355978 um.
#Total half perimeter of net bounding box = 285934 um.
#Total wire length on LAYER metal1 = 9616 um.
#Total wire length on LAYER metal2 = 73013 um.
#Total wire length on LAYER metal3 = 98183 um.
#Total wire length on LAYER metal4 = 63431 um.
#Total wire length on LAYER metal5 = 59529 um.
#Total wire length on LAYER metal6 = 29410 um.
#Total wire length on LAYER metal7 = 14611 um.
#Total wire length on LAYER metal8 = 5394 um.
#Total wire length on LAYER metal9 = 2792 um.
#Total number of vias = 99876

## Slide 24: Verify Design(1/4)
Use command “verifyConnectivity” to detects conditions such as opens, unconnected wires , unconnected pins, loops, etc. And generates violation markers in the design window.
  encounter > verifyConnectivity -type all -error 100 -warning 50

## Slide 25: Verify Design(2/4)
Use command “verifyGeometry” to checks width, spacing, and internal geometry of objects and the wiring between them.
  encounter > verifyGeometry -error 100 -warning 50

## Slide 26: Verify Design(3/4)
Use command “timeDesign” to runs Trial Route, extraction, and timing analysis, and generates detailed timing reports. The generated timing reports are saved in timingReports directory
  encounter > timeDesign -postRoute -hold

## Slide 27: Verify Design(4/4)
s38584_seq_postRoute_hold.summary
# Top Cell: s38584_seq

## Slide 28: Save Design
Save current configuration
  encounter > saveConfig s38584.conf
Save current design
  encounter > saveDesign s38584.enc
Export Netlist for LVS and simulation
  encounter > saveNetlist -includePhysicalInst -excludeLeafCell s38584_lvs.v
Save sdf for post layout simulation
  encounter > delayCal -sdf s38584.sdf

## Slide 29: Outline
Introduction
SOC Encounter
  Scan reorder after Nanoroute
  Scan reorder after placement

## Slide 30: Difference(1/3)
Don’t set command
  encounter > scanReorder
  encounter > routeDesign –globalDetail
  (Re-nano route for scan cell connection part)
Turning scan reorder on and do the placement process
  encounter > setPlaceMode -reorderScan true
  encounter > placeDesign -noPrePlaceOpt

## Slide 31: Difference(2/3)
*** Summary: Scan Reorder
INFO: Finished reorder 20 scan groups.
Initial total scan wire length: 22481.300
Final total scan wire length: 18215.780
Improvement: 4265.520 percent 18.97

## Slide 32: Difference(3/3)
NanoRoute Summary
#Total wire length = 368568 um.
#Total half perimeter of net bounding box = 291070 um.
#Total wire length on LAYER metal1 = 8090 um.
#Total wire length on LAYER metal2 = 77158 um.
#Total wire length on LAYER metal3 = 99475 um.
#Total wire length on LAYER metal4 = 67931 um.
#Total wire length on LAYER metal5 = 62212 um.
#Total wire length on LAYER metal6 = 30815 um.
#Total wire length on LAYER metal7 = 14050 um.
#Total wire length on LAYER metal8 = 6068 um.
#Total wire length on LAYER metal9 = 2768 um.
#Total number of vias = 98985

## Slide 33: Reference
[1] Cadence, “Encounter Menu Reference v8.1”, Nov. 2008
[2] Cadence, “Encounter Text Command Reference v8.1”, Nov. 2008
[3] Cadence , “Encounter User Guide v8.1”, Nov. 2008
[4] IC Lab Course Slide, Chih-Lung Chen