## Slide 1: Verilog HDL Verilog tutorial
E2MATRIX RESEARCH LAB
Opp Phagwara Bus Stand,
Backside Axis Bank, Parmar Complex
Phagwara, Punjab ( India ).
Contact : +91 9041262727
Web : www.e2matrix.com
Email : support@e2matrix.com

## Slide 2: Overview
Simulation and Synthesis
Modules and Primitives
Styles
Structural Descriptions
Language Conventions
Data Types
Delay
Behavioral Constructs
Compiler Directives
Simulation and Testbenches

## Slide 3: Simulation and Synthesis
Simulation tools typically accept full set of Verilog language constructs
Some language constructs and their use in a Verilog description make simulation efficient and are ignored by synthesis tools
Synthesis tools typically accept only a subset of the full Verilog language constructs
  In this presentation, Verilog language constructs not supported in Synopsys FPGA Express are in red italics
  There are other restrictions not detailed here, see [2].

## Slide 4: Modules
The Module Concept
  Basic design unit
  Modules are:
    Declared
    Instantiated
  Modules declarations cannot be nested

## Slide 5: Module Declaration
Annotated Example
/* module_keyword module_identifier (list of ports) */
module C_2_4_decoder_with_enable (A, E_n, D) ;
input [1:0] A ; // input_declaration
input E_n ; // input_declaration
output [3:0] D ; // output_declaration
assign D = {4{~E_n}} & ((A == 2'b00) ? 4'b0001 :
(A == 2'b01) ? 4'b0010 :
(A == 2'b10) ? 4'b0100 :
(A == 2'b11) ? 4'b1000 :
4'bxxxx) ; // continuous_assign
endmodule

## Slide 6: Module Declaration
Identifiers - must not be keywords!
Ports
  First example of signals
  Scalar: e. g., E_n
  Vector: e. g., A[1:0], A[0:1], D[3:0], and D[0:3]
    Range is MSB to LSB
    Can refer to partial ranges - D[2:1]
  Type: defined by keywords
    input
    output
    inout (bi-directional)

## Slide 7: Module Instantiation
module C_4_16_decoder_with_enable (A, E_n, D) ;
input [3:0] A ;
input E_n ;
output [15:0] D ;
wire [3:0] S;
wire [3:0] S_n;
C_2_4_decoder_with_enable DE (A[3:2], E_n, S);
not N0 (S_n, S);
C_2_4_decoder_with_enable D0 (A[1:0], S_n[0], D[3:0]);
C_2_4_decoder_with_enable D1 (A[1:0], S_n[1], D[7:4]);
C_2_4_decoder_with_enable D2 (A[1:0], S_n[2], D[11:8]);
C_2_4_decoder_with_enable D3 (A[1:0], S_n[3], D[15:12]);
endmodule
Example

## Slide 8: Module Instantiation
  Single module instantiation for five module instances
C_2_4_decoder_with_enable DE (A[3:2], E_n, S),
D0 (A[1:0], S_n[0], D[3:0]),
D1 (A[1:0], S_n[1], D[7:4]),
D2 (A[1:0], S_n[2], D[11:8]),
D3 (A[1:0], S_n[3], D[15:12]);
  Named_port connection
C_2_4_decoder_with_enable DE (.E_n (E_n), .A (A[3:2]) .D (S));
// Note order in list no longer important (E_n and A interchanged).
More Examples

## Slide 9: Primitives
Gate Level
  and, nand
  or, nor
  xor, xnor
  buf , not
  bufif0, bufif1, notif0, notif1 (three-state)
Switch Level
  *mos where * is n, p, c, rn, rp, rc; pullup, pulldown; *tran+ where * is (null), r and + (null), if0, if1 with both * and + not (null)

## Slide 10: Primitives
No declaration; can only be instantiated
All output ports appear in list before any input ports
Optional drive strength, delay, name of instance
Example: and N25 (Z, A, B, C); //instance name
Example: and #10 (Z, A, B, X); // delay
(X, C, D, E); //delay
/*Usually better to provide instance name for debugging.*/
Example: or N30 (SET, Q1, AB, N5),
N41 (N25, ABC, R1);
Example: and #10 N33(Z, A, B, X); // name + delay

## Slide 11: Styles
Structural - instantiation of primitives and modules
RTL/Dataflow - continuous assignments
Behavioral - procedural assignments

## Slide 12: Style Example - Structural
module half_add (X, Y, S, C);
input X, Y ;
output S, C ;
xor (S, X, Y) ;
and (C, X, Y) ;
endmodule
module full_add (A, B, CI, S, CO) ;
input A, B, CI ;
output S, CO ;
wire N1, N2, N3;
half_add HA1 (A, B, N1, N2),
HA2 (N1, CI, S, N3);
or P1 (CO, N3, N2);
endmodule

## Slide 13: Style Example - RTL/Dataflow
module fa_rtl (A, B, CI, S, CO) ;
input A, B, CI ;
output S, CO ;
assign S = A ^ B ^ CI; //continuous assignment
assign CO = A & B | A & CI | B & CI; //continuous assignment
endmodule

## Slide 14: Style Example - Behavioral
module fa_bhv (A, B, CI, S, CO) ;
input A, B, CI ;
output S, CO ;
reg S, CO; // required to “hold” values between events.
always@(A or B or CI) //;
begin
S <= A ^ B ^ CI; // procedural assignment
CO <= A & B | A & CI | B & CI; // procedural assignment
end
endmodule

## Slide 15: Structural Descriptions
Textual description of schematic
Form of netlist
Connections
Hierarchy
Arrays of instances
Hierarchy established by instantiation of modules and primitives within modules

## Slide 16: Connections
By position association
  module C_2_4_decoder_with_enable (A, E_n, D);
  C_4_16_decoder_with_enable DX (X[3:2], W_n, word);
  A = X[3:2], E_n = W_n, D = word
By name association
  module C_2_4_decoder_with_enable (A, E_n, D);
  C_2_4_decoder_with_enable DX (.E_n(W_n), .A(X[3:2]), .D(word));
  A = X[3:2], E_n = W_n, D = word

## Slide 17: Connections
Empty Port Connections
  module C_2_4_decoder_with_enable (A, E_n, D);
  C_2_4_decoder_with_enable DX (X[3:2], , word);
    Input E_n is at high-impedance state (z)
  C_2_4_decoder_with_enable DX (X[3:2], W_n ,);
    Output D[3:0] unused.

## Slide 18: Arrays of Instances
{ , } is concatenate
Example
module add_array (A, B, CIN, S, COUT) ;
input [7:0] A, B ;
input CIN ;
output [7:0] S ;
output COUT ;
wire [7:1] carry;
full_add FA[7:0] (A,B,{carry, CIN},S,{COUT, carry});
// instantiates eight full_add modules
endmodule

## Slide 19: Language Conventions
Case-sensitivity
  Verilog is case-sensitive.
  Some simulators are case-insensitive
  Advice: - Don’t use case-sensitive feature!
  Keywords are lower case
Different names must be used for different items within the same scope
Identifier alphabet:
  Upper and lower case alphabeticals
  decimal digits
  underscore

## Slide 20: Language Conventions
Maximum of 1024 characters in identifier
First character not a digit
Statement terminated by ;
Free format within statement except for within quotes
  Strings enclosed in double quotes and must be on a single line
Comments:
  All characters after // in a line are treated as a comment
  Multi-line comments begin with /* and end with */
Compiler directives begin with // synopsys
Built-in system tasks or functions begin with $

## Slide 21: Logic Values
Verilog signal values
  0 - Logical 0 or FALSE
  1 - Logical 1 or TRUE
  x, X - Unknown logic value
  z, Z - High impedance condition
Also may have associated signal and charge strengths for switch level modeling of MOS devices
  7 signal strengths plus 3 charge strengths

## Slide 22: Number Representation
Format: <size><base_format><number>
  <size> - decimal specification of number of bits
    default is unsized and machine-dependent, but at least 32 bits
  <base format> - ' followed by arithmetic base of number
    <d> <D> - decimal - default base if no <base_format> given
    <h> <H> - hexadecimal
    <o> <O> - octal
    <b> <B> - binary
  <number> - value given in base of <base_format>
    _ can be used for reading clarity
    If first character of sized, binary number is 0, 1, the value is 0-filled up to size. If x or z,value is extended using x or z, respectively.

## Slide 23: Number Representation
Examples:
  6’b010_111 gives 010111
  8'b0110 gives 00000110
  8’b1110 gives 00001110
  4'bx01 gives xx01
  16'H3AB gives 0000001110101011
  24 gives 0…0011000
  5'O36 gives 11100
  16'Hx gives xxxxxxxxxxxxxxxx
  8'hz gives zzzzzzzz

## Slide 24: Variables
Nets
  Used for structural connectivity
Registers
  Abstraction of storage (May or may not be real physical storage)
Properties of Both
  Informally called signals
  May be either scalar (one bit) or vector (multiple bits)

## Slide 25: Data Types - Nets - Semantics
wire - connectivity only; no logical
tri - same as wire, but indicates will be 3-stated in hardware
wand - multiple drivers - wired and
wor - multiple drivers - wired or
triand - same as wand, but 3-state
trior - same as wor but 3-state
supply0 - Global net GND
supply1 - Global Net VCC (VDD)
tri0, tri1, trireg

## Slide 26: Net Examples
wire x;
wire x, y;
wire [15:0] data, address;
wire vectored [1:7] control;
wire address = offset + index;
wor interrupt_1, interrupt_2;
tri [31:0] data_bus, operand_bus;
Value implicitly assigned by connection to primitive or module output

## Slide 27: Initial Value & Undeclared Nets
Initial value of a net
  At tsim = 0, initial value is x.
Undeclared Nets - Default type
  Not explicitly declared default to wire
  default_nettype compiler directive can specify others except for supply0 and supply1

## Slide 28: Data Types - Register Semantics
reg - stores a logic value
integer – stores values which are not to be stored in hardware
  Defaults to simulation computer register length or 32 bits whichever is larger
  No ranges or arrays supported
  May yield excess hardware if value needs to be stored in hardware; in such a case, use sized reg.
time - stores time 64-bit unsigned
real - stores values as real num
realtime - stores time values as real numbers

## Slide 29: Register Assignment
A register may be assigned value only within:
  a procedural statement
  a user-defined sequential primitive
  a task, or
  a function.
A reg object may never by assigned value by:
  a primitive gate output or
  a continuous assignment

## Slide 30: Register Examples
reg a, b, c;
reg [15:0] counter, shift_reg;
reg [8:4] flops;
integer sum, difference;

## Slide 31: Strings
No explicit data type
Must be stored in reg whose size is 8*(num. of characters)
reg [255:0] buffer; //stores 32 characters

## Slide 32: Constants (Paramters)
Declaration of parameters
  parameter A = 2’b00, B = 2’b01, C = 2’b10;
  parameter regsize = 8;
    reg [regsize - 1:0]; /* illustrates use of parameter regsize */

## Slide 33: Operators
Arithmetic (binary: +, -,*,/,%*); (unary: +, -)
Bitwise (~, &,|,^,~^,^~)
Reduction (&,~&,|,~|,^,~^,^~)
Logical (!,&&,||,==,!=,===,!==)
Relational (<,<=,>,>=)
Shift (>>,<<)
Conditional ? :
Concatenation and Replications {A,B} {4{B}}
* Not supported for variables

## Slide 34: Expression Bit Widths
Depends on:
  widths of operands and
  types of operators
Verilog fills in smaller-width operands by using zero extension.
Final or intermediate result width may increase expression width

## Slide 35: Expression Bit Widths
Unsized constant number- same as integer (usually 32 bits)
Sized constant number - as specified
x op y where op is +, -, *, /, %, &, |, ^, ^~:
  Arithmetic binary and bitwise
  Bit width = max (width(x), width(y))

## Slide 36: Expression Bit Widths (continued)
op x where op is +, -
  Arithmetic unary
  Bit width = width(x)
op x where op is ~
  Bitwise negation
  Bit width = width(x)

## Slide 37: Expression Bit Widths (continued)
x op y where op is ==, !==, ===, !===, &&, ||, >, >=, <, <= or op y where op is !, &, |, ^, ~&, ~|, ~^
  Logical, relational and reduction
  Bit width = 1
x op y where op is <<, >>
  Shift
  Bit width = width(x)

## Slide 38: Expression Bit Widths (continued)
x ? y : z
  Conditional
  Bit width = max(width(y), width(z))
{x, …, y}
  Concatenation
  Bit width = width(x) + … + width(y)
{x{y, …, z}}
  Replication
  Bit width = x * (width(y) + … + width(z))

## Slide 39: Expressions with Operands Containing x or z
Arithmetic
  If any bit is x or z, result is all x’s.
  Divide by 0 produces all x’s.
Relational
  If any bit is x or z, result is x.
Logical
  == and != If any bit is x or z, result is x.
  === and !== All bits including x and z values must match for equality

## Slide 40: Expressions with Operands Containing x or z
Bitwise
  Defined by tables for 0, 1, x, z operands.
Reduction
  Defined by tables as for bitwise operators.
Shifts
  z changed to x. Vacated positions zero filled.
Conditional
  If conditional expression is ambiguous (e.g., x or z), both expressions are evaluated and bitwise combined as follows: f(1,1) = 1, f(0,0) = 0, otherwise x.

## Slide 41: Simulation Time Scales
Compiler Directive `timescale <time_unit> / <time_precision>
time_unit - the time multiplier for time values
time_precision - minimum step size during simulation - determines rounding of numerical values
Allowed unit/precision values:
{1| 10 | 100, s | ms | us | ns | ps}

## Slide 42: Simulation Time Scales (continued)
Example:
  `timescale 10ps / 1ps
  nor #3.57 (z, x1, x2);
  nor delay used = 3.57 x 10 ps = 35.7 ps => 36 ps
Different timescales can be used for different sequences of modules
The smallest time precision determines the precision of the simulation.

## Slide 43: Behavioral Constructs
Concurrent communicating behaviors => processes same as behaviors
Two constructs
  initial - one-time sequential activity flow - not synthesizable but good for testbenches
  Always - cyclic (repetitive) sequential activity flow
Use procedural statements that assign only register variables (with one exception)

## Slide 44: Behavioral Constructs (continued)
Continuous assignments and primitives assign outputs whenever there are events on the inputs
Behaviors assign values when an assignment statement in the activity flow executes. Input events on the RHS do not initiate activity - control must be passed to the statement.

## Slide 45: Behavioral Constructs (continued)
Body may consist of a single statement or a block statement
A block statement begins with begin and ends with end
Statements within a block statement execute sequentially
Behaviors are an elaborate form of continuous assignments or primitives but operate on registers (with one exception) rather than nets

## Slide 46: Behavioral Constructs - Example
Initial:  Always:
initial always
begin begin
  one = 1; F1 = 0, F2 = 0;
  two = one + 1; # 2 F1 = 1;
  three = two + 1; # 4 F2 = 0;
  four = three + 1; # 2 F1 = 1;
  five = four + 1; # 4;
  end end
What are results of each of the above?

## Slide 47: Procedural Assignments
Types
  = blocking assignment
  assign = continuous assignment
  <= non-blocking assignment
Assignments (with one exception) to:
  reg
  integer
  real
  realtime
  time

## Slide 48: Procedural Assignments - Some Rules
Register variable can be referenced anywhere in module
Register variable can be assigned only with procedural statement, task or function
Register variable cannot be input or inout
Net variable can be referenced anywhere in module
Net variable may not be assigned within behavior, task or function. Exception: force … release
Net variable within a module must be driven by primitive, continuous assignment, force … release or module port

## Slide 49: Procedural Timing, Controls & Synchronization
Mechanisms
  Delay Control Operator (#)
  Event Control Operator (@)*
  Event or
  Named Events – not used much
  wait construct
  *Ignored by FPGA express unless a synchronous trigger that infers a register

## Slide 50: Procedural Timing, Controls & Synchronization
Delay Control Operator (#)
  Precedes assignment statement - postpones execution of statement
  For blocking assignment (=), delays all statements that follow it
  Blocking assignment statement must execute before subsequent statements can execute.
  Example: always @(posedge clk),
      #10 Q = D;

## Slide 51: Procedural Timing, Controls & Synchronization
Event Control Operator (@)*
  Synchronizes the activity flow of a behavior to an event (change) in a register or net variable or expression
  Example 1: @ (start) RegA = Data;
  Example 2: @(toggle) begin
        …
        @ (posedge clk) Q = D;
        …
        end
*Ignored by FPGA express unless a synchronous trigger that infers a register

## Slide 52: Procedural Timing, Controls & Synchronization
Event or - allows formation of event expression
Example:
always @ (X1 or X2 or X3)
assign Y = X1 & X2 | ~ X3;
All RHS variables in sensitivity list and no unspecified conditional results => combinational logic

## Slide 53: Procedural Timing, Controls & Synchronization
Meaning of posedge: 0 -> 1, 0 -> x, x -> 1
Special Example:
always @ (set or reset or posedge clk)
begin
if (reset == 1) Q = 0;
else if (set == 1) Q = 1;
else if (clk == 1) Q = data;
end
// Does this work correctly? Why or why not?

## Slide 54: Procedural Timing, Controls & Synchronization (FIO)
wait Construct
  Suspends activity in behavior until expression following wait is TRUE
Example:
  always
  begin
  a = b;
  c = d;
  wait (advance);
  end

## Slide 55: Blocking Assignments
Identified by =
Sequence of blocking assignments executes sequentially
Example:
always @(posedge clk)
    begin
    b = 0; c = 0;
    b = a + a;
    c = b + a;
    d = c + a;
    end

## Slide 56: Non-Blocking Assignments
Identified by <=
Sequence of non-blocking assignments executes concurrently
Example 1:
always @(posedge clk)
    begin
    b <= 0; c <= 0;
    b <= a + a;
    c <= b + a;
    d <= c + a;
    end
    /*Calculates b = 2a, c = b + a, d <= c + a. All values used on RHS are those at posedge clock. Note that there are two assignments to b and c. Only the last one is effective. */

## Slide 57: Blocking Assignments - Inter-Assignment Delay
Delays evaluation of RHS and assignment to LHS
Example:
always @(posedge clk)
    begin
    b = 0; c = 0;
    b = a + a; // uses a at posedge clock
    #5 c = b + a; // uses a at posedge clock + 5
    d = c + a; // uses a at posedge clock + 5
    end /*c = 2 a(at posedge clock)+ a(at posedge clock + 5)
    d = 2 a(at posedge clock) + 2 a(at posedge clock + 5)*/

## Slide 58
Delays assignment to LHS and subsequent statements, not evaluation of RHS
Example:
always @(posedge clk)
    begin
    b = 0; c = 0;
    b = a + a; // uses a at posedge clock
    c = #5 b + a; // uses a at posedge clock
    d = c + a; // uses a at posedge clock + 5
    end /* c = 3 a(at posedge clock)
    d = 3a (at posedge clock)+ a (at posedge clock + 5)*/
Blocking Assignment - Intra-Assignment Delay

## Slide 59: Non-Blocking Assignment - Inter-Assignment Delay
Delays evaluation of RHS and assignment to LHS
Delays subsequent statements
Example:
always @(posedge clk)
    begin
    b <= 0; c <= 0;
    b <= a + a; // uses a at posedge clock
    #5 c <= b + a; // uses b and a at posedge clock + 5
    d <= c + a; // uses a at posedge clock + 5
    end
    /*c = b(at posedge clock + 5) + a(at posedge clock + 5) d = c(at posedge clock + 5) + a (at posedge clock +5) */

## Slide 60: Non-Blocking Assignment - Intra-Assignment Delay
Delays only assignment to LHS
Example:
always @(posedge clk)
    begin
    b <= 0; c <= 0;
    b <= a + a; // uses a at posedge clock
    c <= #5 b + a; // uses a and b at posedge clock d <= c + a; // uses a and c at posedge clock
    end
    /* Calculates *c(posedge clock + 5) = b(at posedge clock) + a(at posedge clock); d(posedge clock) =
    c(at posedge clock) + a (at posedge clock) */

## Slide 61: Activity Control
Overview
Constructs for Activity Control
  Conditional operator
  case statement
  if … else statement
  Loops : repeat, for, while, forever
  disable statement
  fork … join statement
Tasks and Functions

## Slide 62: Conditional Operator
? … :
Same as for use in continuous assignment statement for net types except applied to register types
Example:
  always@(posedge clock)
    Q <= S ? A : B //combined DFF and 2-to-1 MUX

## Slide 63: case Statement
Requires complete bitwise match over all four values so expression and case item expression must have same bit length
Example: always@(state, x) begin
reg[1:0] state;
  case (state)
  2’b00: next_state <= s1;
  2’b01: next_state <= s2;
  2’b10: if x next_state <= s0;
  else next_state <= s1;
  end
  default next_state = 1’bxx;
  endcase
  end

## Slide 64: casex Statement
Requires bitwise match over all but positions containing x or z; executes first match encountered if multiple matches.
Example:
  always@(code) begin
  casex (code)
  2’b0x: control <= 8’b00100110; //same for 2’b0z
  2’b10: control <= 8’b11000010;
  2’b11: control <= 8’b00111101;
  default control <= 8b’xxxxxxxx;
  endcase
  end

## Slide 65: casez Statement
Requires bitwise match over all but positions containing z or ? (? is explicit don’t care); executes first match encountered if multiple matches.
Example:
  reg [1:0] code;
  always@(code) begin
  casez (code)
  2’b0z: control <= 8’b00100110;
  2’b1?: control <= 8’b11000010;
  default control <= 8b’xxxxxxxx;
  endcase
  end

## Slide 66: Conditional (if … else) Statement Example
  always@(a or b or c) begin
  if (a == b)
  begin
  q <= data;
  stop <= 1’b1;
  end
  else if (a > b)
  q <= a;
  else
  q <= b;
  end
  end
  end

## Slide 67: Conditional (if … else) Statement (continued)
Must be careful to define outcome for all possible conditions – failure do do so can cause unintentional inference of latches!
else is paired with nearest if when ambiguous - use begin and end in nesting to clarify.
Nested if … else will generate a “serial” or priority like circuit in synthesis which may have a very long delay - better to use case statements to get “parallel” circuit.

## Slide 68: for Loop Example
Example:
initial
integer r, i;
begin
r = 0;
for (i = 1; i <= 7; i = i + 2)
begin
r[i] = 1;
end
end

## Slide 69: while Loop Example
initial
begin
r = 0;
i = 0;
while (i <= 7)
begin
r[i] = 1;
i = i + 2;
end
end

## Slide 70: forever Loop Example
initial
begin
clk = 0;
forever
begin
#50 clk = 1;
#50 clk = 0;
end
end
Usually used in testbenches rather than for synthesized logic.

## Slide 71: Tasks
Declared within a module
Referenced only by a behavior within the module
Parameters passed to task as inputs and inouts and from task as outputs or inouts
Local variables can be declared
Recursion not supported although nesting permitted (nested copies of variables use same storage)
See Fig. 7.43 p. 226 of [5]for rules

## Slide 72: Task Example
task leading_1;
input [7:0] data_word;
output [2:0] position;
reg [7:0] temp;
reg [2:0] position;
begin
temp = data_word;
position = 3'b111;
while (!temp[7])
@(posedge clock)
begin
temp = temp << 1;
position = position - 1;
end
end
endtask // Code is not synthesizable

## Slide 73: Functions
Implement combinational behavior
No timing controls or tasks which implies no while
May call other functions with no recursion
Reference in an expression, e.g. RHS
No output or inout allowed
Implicit register having name and range of function

## Slide 74: Function Example
function [2:0] leading_1;
input [7:0] data_word;
reg [7:0] temp;
begin
temp = data_word;
leading_1 = 3'b111;
while (!temp[7])
begin
temp = temp << 1;
leading_1 = leading_1 - 1;
end
end
endfunction
Is the above code synthesizable?
No

## Slide 75: Compiler Directives
Useful for controlling what is synthesized and the resulting logic
Warning: Not recognized by other compilers – therefore reduce code portability
Examples:
  // synopsys translate_off
  Code here describes something that is not to be synthesized such at a simulation testbench -
  can contain non-synthesizable constructs such as delays)
  // synopsys translate_on

## Slide 76: Compiler Directives (Continued)
Examples:
  // synopsys parallel_case
  Forces generation of multiplexer-like structure instead of priority structure when included after case declaration
  // synopsys full_case
  Indicates that all cases have been considered when included in case declaration; when used, no default statement needed and latches will not be inferred can be used in combination with parallel case:
  case (state) // synopsys parallel_case full_case

## Slide 77: Testbench Approach
Use Verilog module to produce testing environment including stimulus generation and/or response monitoring
UUT
Module
Stimulus
Response
Testbench Module

## Slide 78: Stimulus Generation Example
`timescale 1ns /1ns
module com_test_bench_v;
reg[8:0] stim;
wire[3:0] S;
wire C4;
adder_4_b_v a1(stim[8:5], stim[4:1], stim[0], S, C4);
//Continued on next slide
endmodule

## Slide 79: Stimulus Generation Example (Continued)
//Generate stimulus
initial
begin
stim = 9'b000000000;
#10 stim = 9'b111100001;
#10 stim = 9'b000011111;
#10 stim = 9'b111100010;
#10 stim = 9'b000111110;
#10 stim = 9'b111100000;
#10 stim = 9'b000011110;
#10 $stop;
end